## Slide 1: Bits and Bytes Aug. 29, 2002
Topics
  Why bits?
  Representing information as bits
    Binary/Hexadecimal
    Byte representations
      numbers
      characters and strings
      Instructions
  Bit-level manipulations
    Boolean algebra
    Expressing in C
15-213 F’02
class02.ppt
15-213
“The Class That Gives CMU Its Zip!”

## Slide 2: Why Don’t Computers Use Base 10?
Base 10 Number Representation
  That’s why fingers are known as “digits”
  Natural representation for financial transactions
    Floating point number cannot exactly represent $1.20
  Even carries through in scientific notation
    1.5213 X 104
Implementing Electronically
  Hard to store
    ENIAC (First electronic computer) used 10 vacuum tubes / digit
  Hard to transmit
    Need high precision to encode 10 signal levels on single wire
  Messy to implement digital logic functions
    Addition, multiplication, etc.

## Slide 3: Binary Representations
Base 2 Number Representation
  Represent 1521310 as 111011011011012
  Represent 1.2010 as 1.0011001100110011[0011]…2
  Represent 1.5213 X 104 as 1.11011011011012 X 213
Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
  Straightforward implementation of arithmetic functions
0.0V
0.5V
2.8V
3.3V
0
1
0

## Slide 4: Byte-Oriented Memory Organization
Programs Refer to Virtual Addresses
  Conceptually very large array of bytes
  Actually implemented with hierarchy of different memory types
    SRAM, DRAM, disk
    Only allocate for regions actually used by program
  In Unix and Windows NT, address space private to particular “process”
    Program being executed
    Program can clobber its own data, but not that of others
Compiler + Run-Time System Control Allocation
  Where different program objects should be stored
  Multiple mechanisms: static, stack, and heap
  In any case, all allocation within single virtual address space

## Slide 5: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as 0xFA1D37B
      Or 0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 6: Machine Words
Machine Has “Word Size”
  Nominal size of integer-valued data
    Including addresses
  Most current machines are 32 bits (4 bytes)
    Limits addresses to 4GB
    Becoming too small for memory-intensive applications
  High-end systems are 64 bits (8 bytes)
    Potentially address  1.8 X 1019 bytes
  Machines support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 7: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 8: Data Representations
Sizes of C Objects (in Bytes)
  C Data Type Compaq Alpha Typical 32-bit Intel IA32
    int 4 4 4
    long int 8 4 4
    char 1 1 1
    short 2 2 2
    float 4 4 4
    double 8 8 8
    long double 8 8 10/12
    char * 8 4 4
      Or any other pointer

## Slide 9: Byte Ordering
How should bytes within multi-byte word be ordered in memory?
Conventions
  Sun’s, Mac’s are “Big Endian” machines
    Least significant byte has highest address
  Alphas, PC’s are “Little Endian” machines
    Least significant byte has lowest address

## Slide 10: Byte Ordering Example
Big Endian
  Least significant byte has highest address
Little Endian
  Least significant byte has lowest address
Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 11: Reading Byte-Reversed Listings
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example Fragment
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
Deciphering Numbers
  Value: 0x12ab
  Pad to 4 bytes: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00

## Slide 12: Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * creates byte array
typedef unsigned char *pointer;
void show_bytes(pointer start, int len)
{
int i;
for (i = 0; i < len; i++)
printf("0x%p\t0x%.2x\n",
start+i, start[i]);
printf("\n");
}
Printf directives:
  %p: Print pointer
  %x: Print Hexadecimal

## Slide 13: show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux):
int a = 15213;
0x11ffffcb8 0x6d
0x11ffffcb9 0x3b
0x11ffffcba 0x00
0x11ffffcbb 0x00

## Slide 14: Representing Integers
int A = 15213;
int B = -15213;
long int C = 15213;
Decimal: 15213
Binary: 0011 1011 0110 1101
Hex: 3 B 6 D
6D
3B
00
00
Linux/Alpha A
3B
6D
00
00
Sun A
93
C4
FF
FF
Linux/Alpha B
C4
93
FF
FF
Sun B
Two’s complement representation
(Covered next lecture)
00
00
00
00
6D
3B
00
00
Alpha C
3B
6D
00
00
Sun C
6D
3B
00
00
Linux C

## Slide 15: Representing Pointers
int B = -15213;
int *P = &B;
Alpha Address
Hex: 1 F F F F F C A 0
Binary: 0001 1111 1111 1111 1111 1111 1100 1010 0000
01
00
00
00
A0
FC
FF
FF
Alpha P
Sun Address
Hex: E F F F F B 2 C Binary: 1110 1111 1111 1111 1111 1011 0010 1100
Different compilers & machines assign different locations to objects
FB
2C
EF
FF
Sun P
FF
BF
D4
F8
Linux P
Linux Address
Hex: B F F F F 8 D 4 Binary: 1011 1111 1111 1111 1111 1000 1101 0100

## Slide 16: Representing Floats
Float F = 15213.0;
IEEE Single Precision Floating Point Representation
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
15213: 1110 1101 1011 01
Not same as integer representation, but consistent across machines
00
B4
6D
46
Linux/Alpha F
B4
00
46
6D
Sun F
Can see some relation to integer representation, but not obvious
IEEE Single Precision Floating Point Representation
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
15213: 1110 1101 1011 01
IEEE Single Precision Floating Point Representation
Hex: 4 6 6 D B 4 0 0 Binary: 0100 0110 0110 1101 1011 0100 0000 0000
15213: 1110 1101 1011 01

## Slide 17: Representing Strings
char S[6] = "15213";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Other encodings exist, but uncommon
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
    Data are single byte quantities
  Text files generally platform independent
    Except for different conventions of line termination character(s)!
Linux/Alpha S
Sun S
32
31
31
35
33
00
32
31
31
35
33
00

## Slide 18: Machine-Level Code Representation
Encode Program as Sequence of Instructions
  Each simple operation
    Arithmetic operation
    Read or write memory
    Conditional branch
  Instructions encoded as bytes
    Alpha’s, Sun’s, Mac’s use 4 byte instructions
      Reduced Instruction Set Computer (RISC)
    PC’s use variable length instructions
      Complex Instruction Set Computer (CISC)
  Different instruction types and encodings for different machines
    Most code not binary compatible
Programs are Byte Sequences Too!

## Slide 19: Representing Instructions
int sum(int x, int y)
{
return x+y;
}
Different machines use totally different instructions and encodings
00
00
30
42
Alpha sum
01
80
FA
6B
E0
08
81
C3
Sun sum
90
02
00
09
  For this example, Alpha & Sun use two 4-byte instructions
    Use differing numbers of instructions in other cases
  PC uses 7 instructions with lengths 1, 2, and 3 bytes
    Same for NT and for Linux
    NT / Linux not fully binary compatible
E5
8B
55
89
PC sum
45
0C
03
45
08
89
EC
5D
C3

## Slide 20: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
  A&B = 1 when both A=1 and B=1
Not
  ~A = 1 when A=0
Or
  A|B = 1 when either A=1 or B=1
Exclusive-Or (Xor)
  A^B = 1 when either A=1 or B=1, but not both

## Slide 21: Application of Boolean Algebra
A
~A
~B
B
Connection when
A&~B | ~A&B
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A&~B
~A&B
= A^B

## Slide 22: Integer Algebra
Integer Arithmetic
  Z, +, *, –, 0, 1 forms a “ring”
  Addition is “sum” operation
  Multiplication is “product” operation
  – is additive inverse
  0 is identity for sum
  1 is identity for product

## Slide 23: Boolean Algebra
Boolean Algebra
  {0,1}, |, &, ~, 0, 1 forms a “Boolean algebra”
  Or is “sum” operation
  And is “product” operation
  ~ is “complement” operation (not additive inverse)
  0 is identity for sum
  1 is identity for product

## Slide 24
  Commutativity
  A | B = B | A A + B = B + A
  A & B = B & A A * B = B * A
  Associativity
  (A | B) | C = A | (B | C) (A + B) + C = A + (B + C)
  (A & B) & C = A & (B & C) (A * B) * C = A * (B * C)
  Product distributes over sum
  A & (B | C) = (A & B) | (A & C) A * (B + C) = A * B + B * C
  Sum and product identities
  A | 0 = A A + 0 = A
  A & 1 = A A * 1 = A
  Zero is product annihilator
  A & 0 = 0 A * 0 = 0
  Cancellation of negation
  ~ (~ A) = A – (– A) = A
Boolean Algebra  Integer Ring

## Slide 25
  Boolean: Sum distributes over product
  A | (B & C) = (A | B) & (A | C) A + (B * C)  (A + B) * (B + C)
  Boolean: Idempotency
  A | A = A A + A  A
    “A is true” or “A is true” = “A is true”
  A & A = A A * A  A
  Boolean: Absorption
  A | (A & B) = A A + (A * B)  A
    “A is true” or “A is true and B is true” = “A is true”
  A & (A | B) = A A * (A + B)  A
  Boolean: Laws of Complements
  A | ~A = 1 A + –A  1
    “A is true” or “A is false”
  Ring: Every element has additive inverse
  A | ~A  0 A + –A = 0
Boolean Algebra  Integer Ring

## Slide 26: Properties of & and ^
Boolean Ring
  {0,1}, ^, &, , 0, 1
  Identical to integers mod 2
   is identity operation:  (A) = A
    A ^ A = 0
Property Boolean Ring
  Commutative sum A ^ B = B ^ A
  Commutative product A & B = B & A
  Associative sum (A ^ B) ^ C = A ^ (B ^ C)
  Associative product (A & B) & C = A & (B & C)
  Prod. over sum A & (B ^ C) = (A & B) ^ (B & C)
  0 is sum identity A ^ 0 = A
  1 is prod. identity A & 1 = A
  0 is product annihilator A & 0 = 0
  Additive inverse A ^ A = 0

## Slide 27: Relations Between Operations
DeMorgan’s Laws
  Express & in terms of |, and vice-versa
    A & B = ~(~A | ~B)
      A and B are true if and only if neither A nor B is false
    A | B = ~(~A & ~B)
      A or B are true if and only if A and B are not both false
Exclusive-Or using Inclusive Or
    A ^ B = (~A & B) | (A & ~B)
      Exactly one of A and B is true
    A ^ B = (A | B) & ~(A & B)
      Either A is true, or B is true, but not both

## Slide 28: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 29: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j  A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 30: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 --> 0xBE
    ~010000012 --> 101111102
  ~0x00 --> 0xFF
    ~000000002 --> 111111112
  0x69 & 0x55 --> 0x41
    011010012 & 010101012 --> 010000012
  0x69 | 0x55 --> 0x7D
    011010012 | 010101012 --> 011111012

## Slide 31: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 --> 0x00
  !0x00 --> 0x01
  !!0x41 --> 0x01
  0x69 && 0x55 --> 0x01
  0x69 || 0x55 --> 0x01
  p && *p (avoids null pointer access)

## Slide 32: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
    Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
    Useful with two’s complement integer representation
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 33: Cool Stuff with Xor
void funny(int *x, int *y)
{
*x = *x ^ *y; /* #1 */
*y = *x ^ *y; /* #2 */
*x = *x ^ *y; /* #3 */
}
  Bitwise Xor is form of addition
  With extra property that every value is its own additive inverse
    A ^ A = 0
B
A
Begin
B
A^B
1
(A^B)^B = A
A^B
2
A
(A^B)^A = B
3
A
B
End
*y
*x

## Slide 34: Main Points
It’s All About Bits & Bytes
  Numbers
  Programs
  Text
Different Machines Follow Different Conventions
  Word size
  Byte ordering
  Representations
Boolean Algebra is Mathematical Basis
  Basic form encodes “false” as 0, “true” as 1
  General form like bit-level operations in C
    Good for representing & manipulating sets