## Slide 1: CanBus basics
By Robert Leale of CANBusHacks
Edited by Dave Quinton-Schein of figmentofimagination Productions

## Slide 2: Vocabulary
CAN: Controller Area Network
Bus: a type of network where multiple devices transmit on the same physical medium
ECU/ECM: Electronic Control Unit/Module: a small, stand-alone computer with a specific set of tasks
PCB: Printed Circuit Board
OEM: Original Equipment Manufacturer: the “car company” or the company that makes the parts used by the car company, depending on what part you’re talking about

## Slide 3: More Vocab
OBD-II: OnBoard Diagnostics, version 2: USA-mandated connection for all vehicles model year (MY) 1996 and newer
ISO: International Organization for Standardization
SAE: Society of Automotive Engineers
NMEA: National Marine Electronics Association
Tx: Transmitter or Transmitting
Rx: Receiver or Receiving
Noise: electromagnetic interference and/or fluctuating voltage on the bus, which can affect the signal, making 0 look like 1 and 1 look like 0

## Slide 4: Why Canbus?
Modern cars have ~70 ECU (Electronic Control Units)
  ECU manage air bags, brakes, cruise control, powertrain, etc.
  ~100 000 000 lines of code (more than the Boeing 787 Dreamliner)
Connected via “central nervous system” called CAN Bus
  Controller Area Network
  “Multi-master, Broadcast serial bus”
  NO central controller for the network itself
  Every ECU connected to same “line”

## Slide 5: Why CANBUS, continued
ECU communicate via protocols specific to the CAN Bus
  Different manufacturers use different protocols
    “statements” from one car likely will not work on another model
Watching and capturing network traffic can tell us a lot
  Decipher/reverse engineer the captured traffic
  Understand the protocol being used
  Write our own messages- make the car do what we want

## Slide 6: Quick facts
CAN created by Bosch
  http://www.semiconductors.bosch.de/media/pdf/canliteratur/can2spec.pdf
  Early 1990s
  Currently version 2.0B
  Transfer near-real-time data in small frames across a harsh and potentially noisy bus
CAN on PCB (Printed Circuit Board)
  Microprocessor with one or more CAN Controllers as peripherals
  Controller connected to Transceiver
  Transceiver connected to physical layer of the bus
  Provides bi-directional link between the CAN bus and the microprocessor

## Slide 7: Quick Facts, continued
Dominant/Recessive
  0 is Dominant. 1 is Recessive.
  Recessive bits are at the same voltage as an idle line (no ECU transmitting)
  CAN frame built by stringing together these 0s and 1s.

## Slide 8: Physical Layer Protocols
Presently 3 different, main protocols for creating the physical bus:
  Dual-wire CAN
  Fault-tolerant CAN
  Single-wire CAN
All are based on the same concept, but implement it differently

## Slide 9: Dual-Wire High-Speed CAN
Specified by ISO (International Organization for Standardization) 11898-2
Most prevalent physical layer protocol
USA federally-mandated OBD-II (OnBoard Diagnostics, version 2) network for MY (Model Year) 2008 and newer
Used in heavy trucks and agriculture via SAE (Society of Automotive Engineers, and your hosts for the CyberAuto Challenge) J1939
Used in marine industry via NMEA (National Marine Electronics Association) 2000 standard

## Slide 10: Dual-Wire CAN, continued
DWCAN is a “Differential Bus”
  Two, twisted copper wires (a.k.a. “twisted pair”)
    One wire called “CAN High”
    Other wire called “CAN Low”
  Terminated on either end by individual 120-ohm resistors across the CAN high and low wires
    Results in net 60-ohm resistance between the wires
    Necessary for proper signals
    Prevents “signal reflection,” when the signal “bounces back” and interferes with intended signals

## Slide 11: Dual-Wire CAN, continued
Voltage
  “Idle voltage” typically around 2.5 volts
  When “active”, CAN-H line will reach around 3.2v and CAN-L line will reach around 1.8v (1.4v difference, or “delta”)
  Minimum delta is 0.6v
  When this 0.6v delta is true, the bus is Dominant (logical 0)
    Else, it is Recessive (logical 1)

## Slide 12: Single-Wire CAN
SAE J2411
  Low cost alternative to ISO 11898-2
  Only today used by GM
    SWCAN had been used by Honda for several years
  NOT “differential” like 11898-2
    Signaling voltages of 0v at Idle and recessive (logical 1)
    5v for dominant bits (logical 0)
    High Voltage mode to “wake up” nodes that are in low-power state
      Any message greater than 9v
      Typically use “vbatt” (battery voltage)
      Ensures low-power state nodes are able to ignore normal data

## Slide 13: Single-Wire CAN Schematic

## Slide 14: Fault-Tolerant CAN
ISO 11898-3
  Lower-speed, fault-tolerant alternative to ISO 11898-2
  FTCAN can sustain a severed line
    Network recovers to a single-wire topology without modifying any network parameters
  Some OEM are moving away from FTCAN (such as Chrysler and Daimler)
    Others, like Fiat and Hyundai, continue to support it

## Slide 15: Fault-Tolerant CAN Schematic

## Slide 16: CAN Frame Formats (unique to CAN, not borrowed from previous networks
Unique frame format that seems not to borrow from previous network types

## Slide 17: CAN Frame Fields and Default Values
SoF (Start of Frame)
  1 bit
  Denoted by a Dominant Bit on the CAN Bus
Arbitration Field
  For CAN Bus 2.0A or 11 bit frames, the Arbitration field is 12 bits in length
    11 bits of ArbID (Arbitration Identification)
    1 bit of RTR (Remote Transmit Request)
      1 denotes “Remote Frame”
      0 denotes “Data Frame”
      See Frame Types for more information

## Slide 18: CAN Fields and Default Values, Continued
Arbitration Field
  For CAN Bus 2.0B or 29 bit frames, the Arbitration field is 32 bits in length
  29 bits of ArbID
  First 11 ArbID bits at the start
  12: SRR (Substitute Remote Request) bit, set to 0 by default
  13: IDE (Identification, Extended) bit denotes that this is an Extended ID message
    Set to 1
  14-31: next 18 ArbID bits
  32: RTR

## Slide 19: CAN Fields and Default Values, Continued
Control Field
  2 reserved bits (R0 and R1) for backward compatibility in future versions
    Set to 0
  4 bit DLC (Data Length Code)
    Describe total number of bytes in a Data Frame
    Can be used for anything in a Remote Frame
Data Field
  Maximum of 8 bytes of data
CRC (Cyclic Redundancy Check) Field
  16 bit with 2 sections
  Explained more in “CAN Bus Robustness”
  1-bit delimiter give a brief delay to calculate CRC and compare

## Slide 20: CAN Fields and Default Values, Continued
ACK (Acknowledgement Field)
  ACK and ACKd
  Receiving nodes send an “OK” to the Transmitting node
    Tells Tx node that there is at least one Rx node
    Confirms CRC
  Defined as a dominant bit
  All nodes are required to acknowledge, regardless of intended recipient
    Otherwise, must send Error Frame
  ACKd is a recessive bit
    All nodes must remain idle
    If dominant, violates ACKd rules and all nodes must send an Error Frame

## Slide 21: CAN Fields and Default Values, Continued
EoF (End of Frame)
  Section of idle time
  No node allowed to send data
  Allows time for error frames
  8 bits long
Inter-Frame Space
  3 bits of time
  Including 8-bit EoF, allows 11 bits of time between frames

## Slide 22: Bit Timing and Sampling
“Bit Timing” includes “bit width,” “time quanta,” “sync,” “propagation segment,” and “Phase Segments” 1 and 2.
Bit timing serves several purposes, such as resynchronization and sample-point position
Because multiple physical layer protocols exist, need some method for determining the best sample point for a particular baud rate and medium
Each bit is divided into smaller parts called TQ (Time Quanta)
  Each TQ is essentially a place-holder or clock cycle; it’s a measure of a length of time

## Slide 23: Bit Timing and sampling, Continued
Each bit has 4 parts:
  Sync
    1 TQ in length
    Adjusted by special registers in the processor
  PropSeg
    1-8 TQ
  Phase Seg 1
    1-8 TQ
  Phase Seg 2
    1-8 TQ
Sample Point located between PhSeg1 and PhSeg2
  This is where the controller determines Line State (dom or rec)

## Slide 24: Bit Timing and sampling, Continued
Each device on the bus must have the same timing, to avoid errors
Not possible to just guess the timing; must have documentation of original design

## Slide 25: Bit Timing and sampling, Continued
Re-Synchronization
  Since no clock line, CAN Bus must be resynchronized often
Bit Stuffing
  CAN Controller inserts a bit into the frame whenever there have been 5 bits of a single state (dom/rec)
  Bit is of opposite state, ensuring transition on the line
  On any transition, the CAN Controller can re-synch its clock with the others
  Similarly, the stuff bit is removed by Rx controllers
Jump width
  Rules determine how many TQ (forward or backward) the controller is allowed to adjust
  Noisy/harsh environments will usually require a higher Jump Width number

## Slide 26: Frame Types
Data
  Workhorse of CAN- appx 99.999% of all frames
  11-bit or 29-bit
  0-8 bits of data
Remote
  Similar to Data
  Contain no data
  Never used in Automobiles
  Rarely ever used, since Data frames can have 0 bits of data
Error
  6 dom bits followed by 6-12 rec bits
  Sent by Tx or Rx node whenever a violation in CAN rules
  Interrupts messages in progress
  Should not be common on proper wiring with proper controllers

## Slide 27: Modes of Fault Containment
  Isolate faulty hardware to reduce impact
Error Active
  If Rx or Tx node detects an error, sends an “Active Error Frame” as described in Frame Types
    First 6 bits are dominant
  Upon transmission of Error frame, node will increment a counter
    TEC (Tx Error Counter)
    REC (Rx Error Counter)
    REC/TEC greater than or equal to 127 triggers a new state: Error Passive
    TEC decrements upon successful transmission of CAN frame
    REC decrements upon successful receipt of 11 recessive bits

## Slide 28: Modes of Fault Containment, Continued
Error Passive
  When REC or TEC reaches or exceeds 127, node enters Error Passive State
  If Rx or Tx node detects error, sends Passive Error frame
    First 6 bits are *recessive*
    Impossible to detect, since effectively simply idle
    Internal counters increment
  If errors continue, TEC will increment until reaching 255
    Node then set to “Bus Off”
    Only restored via software reset

## Slide 29: Modes of Fault Containment, Continued
Bus Off
  Module not allowed to receive or transmit
  Generally triggered by physical hardware issues on device or connection
  Not a desirable state
  Requires software reset

## Slide 30: CAN Bus Robustness
CRC (Cyclic Redundancy Check)
  Uses CRC-15 (0x62CC Reversed Reciprocal)
  Expects errors to occur
  Catches errors when they occur
  Rx Nodes also calculate CRC for verification
    Error frame may indicate mismatched calculation of CRC
    Error Frame triggers re-send of message
    All Rx nodes will drop previous message

## Slide 31: Media Access Control
CAN Bus uses CSMA/CD (Carrier-Sense, Multiple-Access/Collision Detection)
Multiple-Access
  Any node can start a frame
Carrier-Sense
  Nodes check for an available medium before transmitting
  Means different things in different physical layer protocols
Collision Detection
  Senses if another node is transmitting at the same time- called a “collision”
  Must determine which node gets to continue transmitting
    Called “Arbitration”

## Slide 32: Arbitration
Node with the lower ArbID will not notice the collision
Node with higher ArbID will observe collision and stop transmitting, switching to receiving
Lower ArbID is Higher Priority
Lower priority frame must wait to re-transmit

## Slide 33: Understanding Hexadecimal Numbers
CAN messages use base16 or “Hexadecimal” numbers
While “Decimal” numbers use 0-9 as numerals (10 in total), “Hexadecimal” numbers use 0-9 and A-F as numerals (16 in total)
Customary to use “0x” in front of the values to indicate hex
  0xD would represent the hex value of “D,” or “13”
One hex digit represents 4 binary bits, thus half a byte, and is called a “nibble.”
  To complete the bite, two hex values are used

## Slide 34: Sample CAN Bus Frames
Line 1 has a value of D8 in Byte 1
  1101 1000 in binary
Bytes can represent 0-255, so 0xD8 can mean 216
  OR it could be 0xD = 13 and 0x8 = 8
  OR it could have no decimal meaning at all
If these data represent, say, an odometer reading, then the hex value will represent a decimal number.
If these data represent the status of a driver door (open or closed), then it probably only uses a single bit within that byte
There are hundreds of ways to represent vehicle data using hex… …and all of them will be used.
Solving this puzzle is part of the fun of reverse engineering.

## Slide 35: Recap
CAN is a way for multiple modules to talk to each other on a shared network
0 (dominant) over 1 (recessive)
Three Physical Layers:
  Dual wire (differential), Fault-tolerant, single-wire (non-differential)
Two frame lengths:
  11-bit and 29-bit around data field
  Same Data field size: 0-8 bytes (0-64 bits)
Seven Frame Fields
  Start of Frame, Arbitration, Control, Data, CRC, Acknowledge, End of Frame

## Slide 36: Recap, Cont
Timing controlled within bits and between frames
ReSyncing achieved via bit stuffing
Nodes adjust by *up to* the jump width
  Jump width usually greater on noisy networks
Three modes of fault containment:
  Error Active, Error Passive, Bus Off
Uses CRC-15 for data verification
  Failed CRC confirmation results in error frame
ArbID used to determine priority on the bus
  LOWER ArbID = HIGHER priority